## Slide 1: Patient-Independent MI Localization
MAJOR PROJECT PROGRESS REVIEW
Aryan Kumar • Kunal Maka | NIT Goa | September 2026
Notes: Aryan Kumar and Kunal Maka. Project progress as of 22 September 2026. Research code: https://github.com/Kumaryan12/major_project

## Slide 2: Research question
The published method reports 99.80% accuracy using heartbeat-level evaluation.
We ask whether the same VCG features work on completely unseen patients.
The project reproduces the tensor method, then evaluates patient-level generalization.
Notes: Source: Zhang et al., IEEE TBME 2023, DOI 10.1109/TBME.2022.3202962. The paper's headline result is under its beat-level setup.

## Slide 3: Reproduced tensor pipeline
PTB measured Frank X, Y and Z signals at 1,000 Hz
Wavelet denoising, R-peak detection and 651-sample beats
Lead x time x subband tensor: 3 x 651 x 8
Tucker rank 3 across time gives 72 features
500-tree random forest as the TreeBagger analogue
Notes: Matched PTB cohort: 178 subjects, 425 records, 60,507 detected beats. Paper reports 60,527. See RESULTS.md and configs/paper.yaml.

## Slide 4: The split changes the result
Chart: 
| Random beats | Unseen patients
Result | 99.14 | 41.39
Same PTB cohort and 72-feature model. Beat accuracy (%).
Notes: Both values are beat-level accuracy on the 178-subject PTB cohort. Random beat CV lets the same patient contribute to train and test. Patient-grouped CV has zero patient overlap. Full precision: 99.136% and 41.385%. The published result is 99.80%.

## Slide 5: A learnable patient task
The 12-class task includes MI locations represented by only one patient.
The primary benchmark keeps six classes with at least 10 patients each.
164 patients and 55,863 beats; no patient crosses a test fold.
Primary endpoint: patient-level macro F1.
Notes: Retained classes: AMI, ALMI, ASMI, IMI, ILMI, HC. See BENCHMARK_RESULTS.md and configs/patient_folds.csv.

## Slide 6: Wavelet statistics lead on PTB
Chart: 
| Tucker + SVM | Tucker + RF | Tucker + XGBoost | Wavelet stats + XGBoost
Result | 0.366 | 0.38 | 0.403 | 0.487
Six-class patient macro F1; representation choice needs external confirmation.
Notes: All four results use 164 PTB patients under patient-disjoint evaluation. The wavelet-statistics representation was selected after exploratory ablations on these PTB folds. Nested rerun macro F1: Tucker XGBoost 0.4027; wavelet statistics XGBoost 0.4872. See BENCHMARK_RESULTS.md and ABLATION_RESULTS.md.

## Slide 7: What the feature study showed
Twelve representations tested on frozen patient folds
Wavelet statistics retain lead and subband information without Tucker compression.
Macro F1 improves from 0.403 to 0.487 in the nested PTB comparison.
The tensor model remains the reproduced baseline and scientific comparator.
Notes: Paired class-stratified bootstrap interval for macro-F1 difference: +0.003 to +0.165. This is not independent validation of the representation choice. See ABLATION_RESULTS.md.

## Slide 8: External PTB-XL result
PTB-trained model tested on 1,092 PTB-XL patients with derived VCG
Patient macro F1: 0.242; patient accuracy: 56.23%
Healthy controls are 72.0% of this cohort.
Always predicting healthy would reach 71.98% accuracy.
Notes: Strict PTB-XL fold-10 test: 1,185 ECG records, 1,092 patients. Only 5 ALMI test patients and 0 correct ALMI classifications. No PTB-XL tuning. PTB-XL v1.0.3: https://physionet.org/content/ptb-xl/1.0.3/. See EXTERNAL_RESULTS.md.

## Slide 9: Derived VCG explains only part of the gap
Matched PTB patients: measured → measured VCG macro F1 = 0.469
Measured → derived VCG macro F1 = 0.422
Derived → derived VCG macro F1 = 0.467
The measured-to-derived change is −0.046; its 95% interval includes zero.
Notes: All comparisons use the same 164 PTB patients and matched beat positions. The paired bootstrap interval is -0.108 to +0.017. This isolates the Kors conversion within PTB; it cannot explain all PTB-XL differences. See DOMAIN_SHIFT_RESULTS.md.

## Slide 10: Limits of the current model
The PTB cohort is small for six-class patient prediction.
External labels, recording length and measured versus derived VCG differ.
Some external MI classes have very few patients.
Current results do not support diagnostic use or a state-of-the-art claim.
Notes: Cross-database identity overlap has not been independently verified. External fold 10 has been inspected; any later use should be labeled exploratory unless a new untouched set is obtained.

## Slide 11: Next research phase
Build a compact 1D CNN/ResNet baseline on VCG signals.
Test a tensor-plus-learned-feature hybrid under the same patient folds.
Compare patient macro F1 with uncertainty and seek fresh external validation.
Guide decisions: confirm labels, endpoint, compute and validation plan.
Notes: The deep models and hybrid are proposed work, not yet implemented. Repository: https://github.com/Kumaryan12/major_project. Professor progress report: output/pdf/mi_localization_progress_report.pdf.